ORDINANCE NO.  8-2018

AN ORDINANCE AMENDING CHAPTER 131, FLOOD DAMAGE PREVENTION ORDINANCE, OF THE TOWNSHIP OF MULLICA, COUNTY OF ATLANTIC

WHEREAS, the Township of Mullica has adopted Chapter 131, Flood Damage Prevention Ordinance; and

WHEREAS, the Township of Mullica wishes to amend Chapter 131, to be in compliance and to continue participation in the National Flood Insurance Program; and

NOW, THEREFORE, BE IT ORDAINED, by the Township Committee of the Township of Mullica, in the County of Atlantic and Sate of New Jersey, the cross-out changes are to be deleted and the underlying changes are the changes that are highlighted and will be specifically incorporated into this Ordinance by this reference are hereby adopted and;

BE IT FURTHER ORDAINED that all other terms and conditions as set forth in Chapter 131, shall remain in full force and effect.

This Ordinance shall take effect upon its adoption and publication as provided by law.

CHAPTER 131

131.5 Definitions and word usage.

Advisory Base Flood Elevation (ABFE) - The elevation shown on a community's Advisory Flood Hazard Area Map that indicates the advisory stillwater elevation plus wave effect (ABFE = SWEL + wave effect) resulting from a flood that has a one-percent-or-greater chance of being equaled or exceeded in any given year.

Advisory Flood Hazard Area - The land in the floodplain within a community subject to flooding from the one-percent-annual chance event depicted on the Advisory Flood Hazard Area Map.

Advisory Flood Hazard Area Map - The official map on which the Federal Emergency Management Administration has delineated the areas of advisory flood hazards applicable to the community.

AO Zone- Areas subject to inundation by 1-percent-annual-chance shallow flooding (usually sheet flow on sloping terrain) where average depths are between one and three feet.

AH Zone- Areas subject to inundation by 1-percent-annual-chance shallow flooding (usually areas of ponding) where average depths are between one and three feet. Base Flood Elevations (BFEs) derived from detailed hydraulic analyses are shown in this zone.

Area of Special Flood Hazard - Land in the floodplain within a community subject to a one percent or greater chance of flooding in any given year.  It is shown on the FIRM as Zone V, VE, V1-30, A, AO, A1-A30, AE, A99, or AH.

Base Flood - A flood having a one percent chance of being equaled or exceeded in any given year.

Best Available Flood Hazard Date - The most recent available flood risk guidance FEMA has provided. The best available flood hazard data may be depicted on but not limited to Advisory Flood Hazard Area Maps, Work Maps or Preliminary FIS and FIRM.

Best Available Flood Hazard Data Elevation - The most recent available flood elevation FEMA has provided. The best available flood hazard data elevation may be depicted on an Advisory Flood Hazard Area Map, Work Map, or Preliminary FIS and FIRM.

Elevated Building — A non-basement building (i) built, in the case of a building in an Area of

Special Flood Hazard, to have the top of the elevated floor, elevated above the base flood elevation

plus freeboard by means of piling, columns (posts and piers), or shear walls parallel to the flow of

the water, and (ii) adequately anchored so as not to impair the structural integrity of the building

during a flood up to the magnitude of the base flood.  In an Area of Special Flood Hazard

“elevated building" also includes a building elevated by means of fill or solid foundation perimeter

walls with openings sufficient to facilitate the unimpeded movement of flood waters.

Freeboard - A factor of safety usually expressed in feet above a flood level for purposes of flood

plain management. “Freeboard” tends to compensate for the many unknown factors that could

contribute to flood heights greater than the height calculated for a selected size flood and floodway

conditions, such as wave action, bridge openings, and the hydrological effect of urbanization of

the watershed.

Highest Adjacent Grade - The highest natural elevation of the ground surface prior to

construction next to the proposed or existing walls of a structure.

Lowest Floor - The lowest floor of the lowest enclosed area (including basement).  An unfinished

or flood resistant enclosure, usable solely for the parking of vehicles, building access or storage in

an area other than a basement is not considered a building's lowest floor provided that such

enclosure is not built so to render the structure in violation of other applicable non-elevation design

requirements of 44 CFR Section 60.3.

Manufactured Home - A structure, transportable in one or more sections, which is built on a permanent chassis and is designed for use with or without a permanent foundation when connected to the required utilities. For floodplain management purposes, the term "manufactured home" also includes park trailers, travel trailers and other similar vehicles placed on a site for greater than 180 consecutive days. For insurance purposes, the term "manufactured home" does not include park trailers, travel trailers and other similar vehicles. The term “manufactured home” does not include a “recreational vehicle”.

New Construction - Structures for which the start of construction commenced on or after the effective date of this chapter of a floodplain regulation adopted by a community and includes any subsequent improvements to such structures.

Preliminary Flood Insurance Rate Map (FIRM) - The draft version of the FIRM released for public comment before finalization and adoption.

Sand Dunes - Naturally occurring or man-made accumulations of sand in ridges or mounds landward of the beach.

Start of Construction – (For other than new construction or substantial improvements under the Coastal Barrier Resources Act (P.L. No. 97-348)), includes substantial improvements and means the date the building permit was issued, provided the actual start of construction, repair, reconstruction, rehabilitation, addition, placement, or other improvement was within 180 days of the permit date. The actual start means either the first placement of permanent construction of a structure on a site such as the pouring of a slab or footings, the installation of piles pilings, the construction of columns, or any work beyond the stage of excavation, or the placement of a manufactured home on a foundation. Permanent construction does not include land preparation, such as clearing, grading and filling nor does it include the installation of streets and/or walkways, nor does it include excavation for a basement, footings or piers, or foundations or the erection of temporary forms, nor does it include the installation on the property of accessory buildings, such as garages or sheds not occupied as dwelling units or not part of the main structure. For a substantial improvement, the actual start of construction means the first alteration of any wall, ceiling, floor, or other structural part of a building, whether or not that alteration affects the external dimensions of the building.

#### 131-7 Basis for establishing areas of special flood hazard.

A.	The areas of special flood hazard for the Township of Mullica, Community No. 340517, are identified and defined on the following documents prepared by the Federal Emergency Management Agency:

(1)	A scientific and engineering report "Flood Insurance Study, Township of Mullica, New Jersey, Atlantic County," dated September 1, 1981.

(2)	Flood Insurance Rate Map, Township of Mullica, New Jersey, Atlantic County, as shown on Index and Panel(s) 340517 0005C, 340517 0010C, 340517 0015C, 340517 0016C, 340517 0018C, 340517 0025C, 340517 0026C, the effective date of which is March 1, 1982.

(3)	Flood Boundary and Floodway Map for the Township of Mullica, New Jersey, Atlantic County panels 340517 0001, 340517 002, 340517 0003, 340517 0004, 340517 0005, 340517 0006, the effective date of which is March 1, 1982.

(4)	Best available flood hazard data. These documents shall take precedence over effective panels and FIS in construction and development regulations only. Where the effective mapping or base flood elevation conflict or overlap with the best available flood hazard data, whichever imposes the more stringent requirement shall prevail.

(1)   A scientific and engineering report “Flood Insurance Study, Atlantic County, New Jersey (All Jurisdictions)” dated August 28, 2018.=

(2) 	“Flood Insurance Rate Map for Atlantic County, New Jersey (All Jurisdictions)” as shown on Index and panels 34001C0019F, 34001C0033F, 34001C0040F, 34001C0041F, 34001C0043F, 34001C0044F, 34001C0063F, 34001C0110F, 34001C0130F, 34001C0132F, 34001C0135F, 34001C0140F, 34001C0142F, 34001C0145F, 34001C0151F, 34001C0152F, 34001C0153F, 34001C0154F, 34001C0161F, whose effective date is August 28, 2018.

131.12 Development Permits

A Development Permit shall be obtained before construction or development begins, including placement of manufactured homes, within any area of special flood hazard established in § 131-7.  Application for a Development Permit shall be made on forms furnished by the Zoning Officer  and may include, but not be limited to; plans in duplicate drawn to scale showing the nature, location, dimensions, and elevations of the area in question; existing or proposed structures, fill, storage of materials, drainage facilities; and the location of the foregoing.  Specifically, the following information is required:

131-14. Duties and responsibilities of administration.

D. Alteration of watercourses.  The Zoning Officer shall:

- Notify adjacent communities and the New Jersey Department of Environmental Protection, Bureau of Flood Control and the Land Use Regulation Program prior to any alteration or relocation of a watercourse, and submit evidence of such notification to the Federal Insurance Administration.

- Require that maintenance is provided within the altered or relocated portion of said watercourse so the flood carrying capacity is not diminished.

E. Substantial damage review.  The Zoning Officer Shall:

- After an event resulting in building damages, assess the damage to structures due to flood and non-flood causes.

- Record and maintain the flood and non-flood damage of substantial damage structures and provide a letter of Substantial Damage Determination to the owner and the New Jersey Department of Environmental Protection, Bureau of Flood Control.

- Ensure substantial improvements meet the requirements of sections 131-17A (1), SPECIFIC STANDARDS, RESIDENTIAL CONSTRUCTION, 131-17 B, SPECIFIC STANDARDS, NONRESIDENTIAL CONSTRUCTION and 131-17C SPECIFIC STANDARDS, MANUFACTURED HOMES.

F.   Interpretation of FIRM boundaries. Make interpretations, where needed, as to the exact location of the boundaries of the areas of special flood hazards (for example, where there appears to be a conflict between a mapped boundary and actual field conditions). The person contesting the location of the boundary shall be given a reasonable opportunity to appeal the interpretation as provided in § 131-15.

131-15 B. Conditions for Variances.

(2)   	Variances may be issued for the reconstruction, rehabilitation or restoration of structures 	listed on the National Register of Historic Places or the State Inventory of Historic 	Places, without regard to the procedures set forth in the remainder of this section. Variances 	may be issued for the repair or rehabilitation of historic structures upon a determination that 	the proposed repair or rehabilitation will not preclude the structure's continued designation 	as a historic structure and the variance is the minimum necessary to preserve the historic 	character and design of the structure

131-16. General Standards for flood hazard reduction.

A. Anchoring

(2)       All manufactured homes to be placed or substantially improved shall be anchored to  		resist flotation, collapse or lateral movement. Methods of anchoring may include but 		are not 	to be limited to use of over-the-top or frame ties to ground anchors. This 			requirement is in addition to applicable state and local anchoring requirements 			for resisting wind forces. Special requirements shall be that:

C. Utilities.

(4)	For all new construction and substantial improvements the electrical, heating, ventilation, plumbing and air-conditioning equipment and other service facilities shall be designed and/or located so as to prevent water from entering or accumulating within the components during conditions of flooding.

E.  	Enclosure openings. All new construction and substantial improvements having fully

enclosed areas below the lowest floor that are usable solely for parking of vehicles, building access or storage in an area other than a basement and which are subject to flooding shall be designed to automatically equalize hydrostatic flood forces on exterior walls by allowing for the entry and exit of floodwaters.  Designs for meeting this requirement must either be certified by a registered professional engineer or architect or must meet or exceed the following minimum criteria: A minimum of two (2) openings in at least two (2) exterior walls of each enclosed area, having a total net area of not less than one (1) square inch for every square foot of enclosed area subject to flooding shall be provided. The bottom of all openings shall be no higher than one (1) foot above grade.  Openings may be equipped with screens, louvers, or other covering or devices provided that they permit the automatic entry and exit of floodwaters.

131-17. Specific Standards for flood hazard reduction.

A. Residential construction.

- New construction and substantial improvement of any residential structure located in                          an A or AE zone shall have the lowest floor, including basement together with the attendant utilities (including all electrical, heating, ventilating, air- conditioning and other service equipment) and sanitary facilities, elevated at or above the base flood elevation plus two (2) feet or as required by ASCE/SEI 24-14, Table 2-1, whichever is more restrictive

- Require within any AO or AH zone on the municipality's DFIRM that all new construction and substantial improvement of any residential structure shall have the lowest floor, including basement together with the attendant utilities and sanitary facilities, elevated above the depth number specified in feet plus two (2) feet, above the highest adjacent grade (at least four (4) feet if no depth number is specified).  And, require adequate drainage paths around structures on slopes to guide floodwaters around and away from proposed structures.

B. Nonresidential construction. In an Area of Special Flood Hazard, all new construction and

substantial improvement of any commercial, industrial or other nonresidential structure located

in an A or AE zone shall have the lowest floor, including basement together with the attendant

utilities and sanitary facilities as well as all electrical, heating, ventilating, air-conditioning and

other service equipment:

Either

- Elevated to or above the base flood elevation plus two (2) feet or as required by ASCE/SEI

24-14, Table 2-1, whichever is more restrictive; and

- Require within any AO or AH zone on the municipality's DFIRM to elevate above the depth

number specified in feet plus two (2) feet, above the highest adjacent grade (at least four (4) feet if no depth number is specified).  And, require adequate drainage paths around structures on slopes to guide floodwaters around and away from proposed structures;

or

- Be flood proofed so that below the base flood level plus two (2) feet or as required by

ASCE/SEI 24-14, Table 6-1, whichever is more restrictive, the structure is watertight with walls substantially impermeable to the passage of water;

- Have structural components capable of resisting hydrostatic and hydrodynamic loads and

effects of buoyancy; and,

- Be certified by a registered professional engineer or architect that the design and methods

of construction are in accordance with accepted standards of practice for meeting the applicable provisions of this subsection.  Such certification shall be provided to the official as set forth in § 131-14C (2).

C. Manufactured homes.

(1) Manufactured homes shall be anchored in accordance with Section 131-16A (2).

(2) All manufactured homes to be placed or substantially improved within an area of special

flood hazard shall:

- Be consistent with the need to minimize flood damage,

- Be constructed to minimize flood damage,

- Have adequate drainage provided to reduce exposure to flood damage,

- Be elevated on a permanent foundation such that the top of the lowest floor is at or above the base flood elevation plus two (2) feet or as required by ASCE/SEI 24-14, Table 2-1, whichever is more restrictive and;

- The manufactured home chassis is supported by reinforced piers or other

foundation elements of at least equivalent strength that are no less than 36 inches

in height above grade and be securely anchored to an adequately anchored

foundation system to resist floatation, collapse, and lateral movement.

131-18. Floodways

C. The placement of any mobile homes, except in an existing mobile home park or existing mobile home subdivision, is prohibited.

131-20 Severability. If any section, subsection, paragraph, sentence, clause, or phrase of this Ordinance shall be declared invalid for any reason whatsoever, such a decision shall not affect the remaining portions of the Ordinance, which shall remain in full force and effect, and for this purpose the provisions of this Ordinance are hereby declared to be severable.

131-21. Adoption. This Ordinance shall be effective on (effective date) and shall remain in force until modified, amended or rescinded by Township of Mullica, County of Atlanitc, State of New Jersey.

First Reading:  June 12, 2018

Adoption:	 June 26, 2018

________________________________

CHRISTOPHER SILVA, MAYOR

ATTEST:

_____________________________

KIMBERLY JOHNSON, RMC